## Slide 1
WIRELESS TECHNOLOGY MASTERCLASS
IEEE 802.15.4, Zigbee & Thread
From high-level user concepts to deep protocol internals
A structured bridge for the Bluetooth engineer
IEEE 802.15.4
The PHY + MAC foundation
Zigbee
Application-rich mesh stack
Thread
IPv6 low-power mesh
Learning goal: understand every technical discussion · define products & features · read the market

## Slide 2
How to Read This Deck
Structured from user-level down to bit-level — you can stop at any depth
802.15.4 · Zigbee · Thread — Technical Masterclass
2
▸ Part 1 — The Landscape
  • Where these fit in the IoT wireless world
  • Mental model mapped from your Bluetooth knowledge
▸ Part 2 — IEEE 802.15.4 (the foundation)
  • PHY, MAC, channels, frames, topologies
▸ Part 3 — Zigbee (the application stack)
  • NWK, APS, ZCL/ZDO, clusters, security
▸ Part 4 — Thread (the IP stack)
  • 6LoWPAN, IPv6, roles, commissioning, security
▸ Part 5 — Compare · Matter · Products · Future
The one-sentence mental model
▸ 802.15.4 = the radio + link layer
  • Like BT's PHY + Link Layer. It moves frames; it does not define apps.
▸ Zigbee = full stack ON TOP of 802.15.4
  • Adds mesh routing + a rich application language (clusters).
▸ Thread = IPv6 stack ON TOP of 802.15.4
  • Adds 6LoWPAN + IPv6/UDP mesh. App layer is separate (e.g. Matter).
▸ Matter = common app layer over Thread/Wi-Fi

## Slide 3
The IoT Wireless Landscape
Every technology trades range, data rate, power and topology differently
802.15.4 · Zigbee · Thread — Technical Masterclass
3
Technology | Band | Raw rate | Range | Topology | Sweet spot
Bluetooth LE | 2.4 GHz | 1–2 Mbps | 10–100 m | Star / Mesh | Phone-centric, audio, wearables
802.15.4 / Zigbee | 2.4 GHz / sub-GHz | 250 kbps | 10–100 m | Mesh | Home/building sensor & control mesh
Thread | 2.4 GHz | 250 kbps | 10–100 m | IPv6 Mesh | IP-native smart home (Matter)
Wi-Fi | 2.4/5/6 GHz | 10 Mbps–Gbps | 20–50 m | Star (AP) | High-bandwidth, mains-powered
LoRaWAN / NB-IoT | sub-GHz / cellular | 0.3–50 kbps | km scale | Star | Long-range, tiny payloads
Key insight: 802.15.4 / Zigbee / Thread live in the SAME 2.4 GHz neighbourhood as Bluetooth and Wi-Fi, but are engineered for many low-power nodes forming self-healing MESH networks — not for streaming.

## Slide 4
Bridge From What You Know: Bluetooth ↔ These Stacks
Same OSI ideas, different names
802.15.4 · Zigbee · Thread — Technical Masterclass
4
OSI-ish layer | Bluetooth LE | Zigbee | Thread
Application | GATT profiles / services | Zigbee Cluster Library (ZCL) | Matter / CoAP / app of choice
App support | ATT / GATT | APS (App Support Sublayer) | UDP + DTLS
Network / routing | L2CAP + BT Mesh (opt.) | Zigbee NWK (mesh routing) | IPv6 + 6LoWPAN + MLE routing
Link / MAC | Link Layer | IEEE 802.15.4 MAC | IEEE 802.15.4 MAC
Physical (radio) | BLE PHY (GFSK 2.4 GHz) | IEEE 802.15.4 PHY (O-QPSK) | IEEE 802.15.4 PHY (O-QPSK)
Takeaway: Zigbee and Thread SHARE the bottom two layers (802.15.4 PHY+MAC). They diverge above the MAC — Zigbee builds its own network+app world; Thread runs standard IPv6.

## Slide 5
01
IEEE 802.15.4 — The Foundation
The PHY and MAC that both Zigbee and Thread stand on
802.15.4 · Zigbee · Thread — Technical Masterclass
5

## Slide 6
What IEEE 802.15.4 Actually Is
A standard for Low-Rate Wireless Personal Area Networks (LR-WPAN)
802.15.4 · Zigbee · Thread — Technical Masterclass
6
▸ Defines ONLY the two lowest layers
  • PHY (physical radio) and MAC (medium access control)
  • Deliberately stops there — upper stacks (Zigbee, Thread, WirelessHART, ISA100, Matter-over-Thread) build on top
▸ Design goals
  • Ultra low power (coin-cell, years of life)
  • Low cost, low complexity silicon
  • Robust in noisy 2.4 GHz environments
  • Support many nodes & mesh-friendly links
▸ First published 2003; revised 2006, 2011, 2015, 2020
Analogy for a BT engineer
▸ 802.15.4 ≈ the BLE Controller (PHY + Link Layer).
▸ It gives you: channels, modulation, framing, addressing, CSMA-CA, ACKs, and a MAC state machine.
▸ It does NOT give you: routing, services, security keys management, or apps.
▸ That gap is exactly why Zigbee and Thread exist.

## Slide 7
802.15.4 PHY — The Radio
Bands, channels and modulation
802.15.4 · Zigbee · Thread — Technical Masterclass
7
▸ Three main band options
  • 2.4 GHz ISM — global, 16 channels, 250 kbps (most common)
  • 915 MHz (Americas) — 10 channels, 40 kbps
  • 868 MHz (Europe) — 1 channel, 20 kbps
▸ 2.4 GHz PHY details
  • Channels 11–26, spaced 5 MHz apart
  • Modulation: O-QPSK with DSSS (spreading) — robust vs interference
  • Chip rate 2 Mchip/s → 250 kbps effective
▸ Transmit power typically 0 dBm (1 mW); range ~10–100 m
▸ Coexists with Wi-Fi — channels 15, 20, 25, 26 dodge common Wi-Fi
2.4 GHz channel map (11–26)
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
Green = quieter vs typical Wi-Fi ch 1/6/11
vs Bluetooth PHY
▸ BLE: 40 ch × 2 MHz, GFSK, adaptive frequency hopping.
▸ 802.15.4: 16 ch × 5 MHz, O-QPSK/DSSS, NO hopping — picks one channel and stays (spreading gives robustness).

## Slide 8
802.15.4 MAC — Medium Access & Framing
How nodes share the air and build links
802.15.4 · Zigbee · Thread — Technical Masterclass
8
▸ Channel access: CSMA-CA
  • Listen-before-talk; random backoff to avoid collisions
  • Optional slotted mode with superframe + beacons (GTS for QoS)
▸ Four MAC frame types
  • Beacon — network timing / presence
  • Data — carries the payload
  • Acknowledgment — reliable delivery
  • MAC command — association, disassociation, etc.
▸ Addressing
  • 64-bit extended (EUI-64, globally unique) OR
  • 16-bit short address (assigned on join, saves space)
  • 16-bit PAN ID identifies the network
MAC frame anatomy
MHR
Frame Control
Seq#
Addr fields
Payload
FCS
Max PHY payload 127 bytes → tight! Drives header compression in Thread (6LoWPAN).
Device types (MAC level)
▸ FFD — Full-Function Device: can route, be coordinator.
▸ RFD — Reduced-Function Device: leaf/end node, sleepy, talks only to its parent.

## Slide 9
802.15.4 RF + Link Layer Capability Deep Dive
The details that drive real product performance
802.15.4 · Zigbee · Thread — Technical Masterclass
9
▸ RF capabilities
  • Energy Detect (ED) for channel surveys and adaptive channel planning
  • CCA modes (energy, carrier, carrier+energy) feed CSMA-CA decisions
  • DSSS processing gain improves resilience in noisy ISM environments
▸ MAC capabilities
  • Unslotted/slotted CSMA-CA with tunable BE/backoff/retry parameters
  • ACK request + retry limit settings shape reliability vs latency
  • Indirect data + frame-pending bit enables sleepy battery children
  • Beacon superframe with optional GTS enables deterministic windows
▸ Security at link layer
  • AES-128-CCM* with frame counters and MIC for replay protection
Deployment tuning playbook
▸ Channel plan first
  • Avoid Wi-Fi overlap; prioritize ch 15/20/25/26 when practical
▸ Budget airtime
  • Keep payloads compact; 127-byte PHY frame cap is absolute
▸ Tune MAC
  • Raise retries for reliability; lower retries for latency-sensitive control
  • Tune child poll intervals to trade battery life vs downlink responsiveness
▸ Design for coexistence
  • Measure ED/CCA fail rate + retry counters during field trials

## Slide 10
802.15.4 Topologies
From simple star to self-healing mesh
802.15.4 · Zigbee · Thread — Technical Masterclass
10
Star
One coordinator, all nodes talk to it. Simple, single point of failure.
Cluster tree
Coordinator + routers form a tree; extends range hop-by-hop.
Mesh
Routers interconnect; multiple paths → self-healing & resilient.
Zigbee and Thread both use MESH. Mains-powered routers relay for battery 'end devices' that sleep. Add a device → the mesh grows and finds new paths automatically; remove one → traffic reroutes.

## Slide 11
02
Zigbee — The Application Stack
Mesh routing + a rich, interoperable device language on top of 802.15.4
802.15.4 · Zigbee · Thread — Technical Masterclass
11

## Slide 12
The Zigbee Stack At A Glance
Everything above the 802.15.4 MAC is 'Zigbee'
802.15.4 · Zigbee · Thread — Technical Masterclass
12
Application layer — your device logic + ZCL clusters
APS — Application Support Sublayer (binding, endpoints, groups)
ZDO — Zigbee Device Object (discovery, roles, network mgmt)
NWK — Network layer (mesh routing, addressing, security)
IEEE 802.15.4 MAC
IEEE 802.15.4 PHY (2.4 GHz / sub-GHz radio)
Zigbee = NWK + APS + ZDO + ZCL, standardized by the Connectivity Standards Alliance (CSA).
What each layer buys you
▸ NWK
  • Mesh routing (AODV-style), 16-bit addresses, network key security
▸ APS
  • Endpoints, bindings, groups; reliable end-to-end delivery
▸ ZDO
  • Device & service discovery, join/leave, role management
▸ ZCL
  • The shared 'vocabulary' of attributes & commands that makes brands interoperate

## Slide 13
Zigbee Device Roles
Three roles define the mesh
802.15.4 · Zigbee · Thread — Technical Masterclass
13
Coordinator (ZC)
▸ Exactly ONE per network
▸ Forms the network, picks channel + PAN ID
▸ Holds trust-center security role
▸ Always powered; often the hub/gateway
Router (ZR)
▸ Mains-powered, always on
▸ Relays packets → extends the mesh
▸ Can host application endpoints too
▸ e.g. smart bulbs, plugs act as routers
End Device (ZED)
▸ Battery-powered, sleepy (RFD)
▸ Talks only to ONE parent router
▸ Cannot relay for others
▸ e.g. door sensor, remote, thermostat
Mental check: a smart bulb is a Router (always powered, extends mesh); a battery PIR sensor is an End Device (sleeps to save power). More mains-powered devices = stronger mesh.

## Slide 14
Zigbee Application Model: Endpoints, Clusters, Attributes
The part that defines PRODUCTS and FEATURES
802.15.4 · Zigbee · Thread — Technical Masterclass
14
▸ Node → Endpoints (1–240)
  • One physical device can expose many endpoints (e.g. a 2-gang switch = 2 endpoints)
▸ Endpoint → Clusters
  • A cluster = a feature module (On/Off, Level, Color Control, Temperature Measurement…)
  • Server side hosts attributes; Client side controls them
▸ Cluster → Attributes + Commands
  • Attribute = a state value (e.g. CurrentLevel = 0–254)
  • Command = an action (e.g. Move to Level, Toggle)
▸ Binding & Groups
  • Binding links a switch's client cluster to a bulb's server cluster — direct control
  • Groups = one command to many devices (whole-room off)
Worked example: a smart dimmer bulb
▸ Endpoint 1
  • On/Off cluster → attribute OnOff, cmd Toggle
  • Level Control → attr CurrentLevel, cmd Move to Level
  • Color Control → attrs Hue/Saturation/ColorTemp
  • Identify, Basic, Groups, Scenes clusters
▸ Because clusters are standardized…
  • A Philips Hue switch can drive an IKEA bulb — same On/Off & Level cluster semantics. THIS is interoperability.

## Slide 15
Zigbee Networking & Routing
How a packet crosses the mesh
802.15.4 · Zigbee · Thread — Technical Masterclass
15
▸ Addressing
  • 64-bit IEEE address (permanent) + 16-bit NWK short address (assigned at join)
▸ Mesh routing (AODV-derived)
  • Route discovery floods a Route Request; best path replies with Route Reply
  • Routers keep a routing table + route to next hop
  • Many-to-one routing optimizes 'everyone → gateway' traffic
▸ Reliability
  • MAC ACK per hop + optional APS ACK end-to-end
▸ Joining
  • Permit-join window; device associates to a parent, gets keys & short address
Multi-hop delivery
Sensor
Router
Router
Gateway
Each hop: CSMA-CA + MAC ACK. Battery sensor sleeps; its parent buffers messages until it polls.
Note: classic Zigbee needs a HUB/gateway to bridge to IP/cloud. This is a key contrast with Thread.

## Slide 16
Zigbee Security
AES-128 everywhere, managed by a Trust Center
802.15.4 · Zigbee · Thread — Technical Masterclass
16
▸ Cryptography
  • AES-128-CCM* provides encryption + integrity (MIC) at NWK and APS layers
▸ Key hierarchy
  • Network key — shared by all nodes; secures mesh-wide traffic
  • Link key — pairwise between two devices; secures APS end-to-end and key transport
  • Trust Center Link Key — used when joining to receive the network key
▸ Trust Center
  • Usually the Coordinator; authorizes joins and distributes/rotates keys
▸ Zigbee 3.0 hardened onboarding
  • Install codes (per-device pre-shared secret) → unique link key, no well-known default key
  • Unified profile: one interoperable Zigbee 3.0 replaces old Home Automation / Light Link profiles
▸ Historical weak spot: legacy devices used a well-known default Trust Center key — Zigbee 3.0 install codes fix this.

## Slide 17
Zigbee Capability Matrix
What Zigbee gives you beyond raw connectivity
802.15.4 · Zigbee · Thread — Technical Masterclass
17
▸ Application capabilities
  • Standard ZCL clusters for lighting, metering, HVAC, occupancy and security
  • Groups + Scenes for low-latency room-wide automation
▸ Network capabilities
  • Self-healing mesh routing with route discovery and repair
  • Many-to-one optimization for 'all nodes to gateway' telemetry
▸ Operational capabilities
  • Strong battery model: sleepy end devices + parent buffering
  • Mature certification and massive installed base ecosystem
▸ Integration capabilities
  • Bridge into IP/Matter ecosystems via hub/gateway translation
Product-fit guidance
▸ Best fit
  • Lighting/sensor/control networks with high device count
  • Cost-sensitive products needing proven module ecosystem
▸ Watch-outs
  • Gateway architecture quality decides UX and cloud latency
  • Channel planning and router density decide mesh stability
▸ Forward strategy
  • Ship Zigbee now, expose to Matter through bridges, keep migration path

## Slide 18
03
Thread — The IPv6 Mesh
Standard Internet Protocol, down to the tiny sensor
802.15.4 · Zigbee · Thread — Technical Masterclass
18

## Slide 19
What Makes Thread Different
It is IP — every node has an IPv6 address
802.15.4 · Zigbee · Thread — Technical Masterclass
19
▸ Same radio & MAC as Zigbee
  • IEEE 802.15.4 (2.4 GHz, 250 kbps, mesh)
▸ But the network layer is native IPv6
  • 6LoWPAN compresses IPv6 to fit 127-byte frames
  • UDP transport; CoAP/DTLS for messaging + security
  • No application layer of its own → app is separate (Matter)
▸ Designed by Thread Group (Nest/Google origin, 2014)
▸ Key benefits
  • No single hub bottleneck — self-healing, no single point of failure
  • Border Router bridges Thread ↔ Wi-Fi/Ethernet at the IP level
  • End-to-end IP means cloud/app can address a bulb directly
Thread stack
Application (Matter, CoAP…)
UDP + DTLS
IPv6 + routing (MLE, RPL-like)
6LoWPAN adaptation (compression)
IEEE 802.15.4 MAC
IEEE 802.15.4 PHY

## Slide 20
Thread Device Roles
Roles are dynamic — the mesh self-organizes
802.15.4 · Zigbee · Thread — Technical Masterclass
20
Border Router
▸ Bridges Thread ↔ Wi-Fi/Ethernet (IP)
▸ Can have MANY per network (redundant)
▸ e.g. HomePod mini, Nest Hub, Eero
Leader
▸ One elected router that manages the mesh
▸ Assigns router IDs, holds network data
▸ If it fails, another is auto-elected
Router
▸ Forwards packets, always on
▸ Keeps mesh connectivity & routes
▸ REED can promote to Router as needed
End Device (MED/SED)
▸ Minimal/Sleepy End Device (battery)
▸ Talks to a parent router only
▸ Sleeps for years on a coin cell
Self-healing in action: lose the Leader → re-election; lose a Border Router → another takes over; no manual reconfiguration. Roles (Leader/Router/REED) shift automatically as devices come and go.

## Slide 21
Thread: Networking & Commissioning
How a device joins and how packets flow
802.15.4 · Zigbee · Thread — Technical Masterclass
21
▸ Addressing
  • Every node gets IPv6 addresses (link-local + mesh-local + optional global)
  • RLOC (Routing Locator) encodes position in the mesh
▸ Routing
  • Routers exchange MLE (Mesh Link Establishment) to maintain link quality & routes
  • Distance-vector routing among routers; end devices via their parent
▸ Commissioning (secure onboarding)
  • New 'Joiner' + 'Commissioner' (phone/app) authenticate via a PSKd/passphrase
  • DTLS handshake (J-PAKE) → device receives network credentials
  • Matter uses a QR/setup code that carries the onboarding secret
▸ Multicast & service discovery via IPv6 — no proprietary binding needed
Border Router: the key idea
Cloud / App
Border Router
Wi-Fi / Ethernet (IPv6)
Because the Border Router speaks IPv6 both sides, your phone app addresses a Thread bulb like any internet host — no protocol translation gateway.

## Slide 22
Thread Security
Secure by default, at multiple layers
802.15.4 · Zigbee · Thread — Technical Masterclass
22
▸ Network-wide MAC security
  • All 802.15.4 frames encrypted + authenticated with AES-128-CCM using the network key
▸ Application/transport security
  • DTLS secures commissioning and app messaging (CoAP over UDP)
▸ Onboarding
  • J-PAKE password-authenticated key exchange — device proves it knows the passphrase without sending it
  • Only authenticated devices ever receive the network credentials
▸ Operational hardening
  • Key rotation supported; no device can join without the commissioning secret
  • Mesh-local addressing keeps internal traffic off the global internet by default
▸ Result: Thread was designed 'secure-first' — every joined node is authenticated and every frame is encrypted.

## Slide 23
Thread Capability Matrix
IP-native strengths and design trade-offs
802.15.4 · Zigbee · Thread — Technical Masterclass
23
▸ Networking capabilities
  • Native IPv6 end-to-end addressing per node
  • 6LoWPAN compression + fragmentation for constrained 802.15.4 frames
  • Self-healing role-based mesh (Leader/Router/REED/End Device)
▸ Platform capabilities
  • Multiple Border Routers for redundancy and failover
  • No single coordinator bottleneck in steady-state operation
▸ Application capabilities
  • Ideal transport for Matter with standard IP tooling and telemetry
▸ Security capabilities
  • Secure commissioning + authenticated membership by design
Product-fit guidance
▸ Best fit
  • Future-facing smart-home products targeting Matter ecosystems
  • Products needing IP-native operations and cloud/app observability
▸ Watch-outs
  • Border Router quality and placement strongly affect onboarding UX
  • Still needs careful channel planning in crowded 2.4 GHz spaces
▸ Forward strategy
  • Use multiprotocol SoCs: BLE for commissioning + Thread for mesh data plane

## Slide 24
04
Compare · Matter · Market · Future
Putting it all together for product decisions
802.15.4 · Zigbee · Thread — Technical Masterclass
24

## Slide 25
Zigbee vs Thread vs Bluetooth Mesh
The decision matrix
802.15.4 · Zigbee · Thread — Technical Masterclass
25
Dimension | Zigbee | Thread | Bluetooth Mesh
Radio / MAC | 802.15.4 | 802.15.4 | BLE (2.4 GHz)
Network layer | Zigbee NWK (proprietary) | Native IPv6 | Managed-flood (no routing tables)
IP-addressable | No (needs gateway) | Yes (per node) | No
App layer | ZCL clusters (built-in) | Separate (Matter/CoAP) | BT Mesh models
Hub needed | Yes (coordinator/gateway) | Border Router (IP bridge) | Provisioner; phone-friendly
Interop story | Zigbee 3.0 certified | Matter over Thread | Mesh models / Matter (emerging)
Best for | Mature sensor/control mesh | Future-proof IP smart home | Phone-provisioned, lighting

## Slide 26
Matter — Why It Changes Everything
The common application layer that rides on Thread (and Wi-Fi)
802.15.4 · Zigbee · Thread — Technical Masterclass
26
▸ What Matter is
  • An application-layer standard (CSA) for smart-home interoperability
  • Runs OVER Thread or Wi-Fi (and uses BLE only for commissioning)
▸ Why it matters for you
  • Separates 'app language' from 'transport' — Thread carries IP; Matter defines device types
  • Backed by Apple, Google, Amazon, Samsung → cross-ecosystem
▸ Matter data model echoes Zigbee's
  • Nodes → Endpoints → Clusters → Attributes/Commands (familiar!)
  • In fact ZCL heavily influenced Matter's data model
▸ Zigbee's clusters concept lives on inside Matter — your Zigbee knowledge transfers directly.
Where each layer sits
Matter (device types, clusters)
Thread OR Wi-Fi (transport)
802.15.4 / IPv6 | IP
Radio
BLE is used only to commission a Matter device onto Thread/Wi-Fi.

## Slide 27
Products In The Market Today
Where you'll actually meet these stacks
802.15.4 · Zigbee · Thread — Technical Masterclass
27
▸ Zigbee — shipping at huge scale
  • Philips Hue lighting (bridge + bulbs)
  • IKEA TRÅDFRI / DIRIGERA
  • Samsung SmartThings hub & sensors
  • Amazon Echo (4th gen) built-in Zigbee hub
  • Aqara, Sonoff, Tuya sensors & switches
  • Industrial: metering, building automation
▸ Thread — rapidly expanding
  • Apple HomePod mini / HomePod (Border Router)
  • Google Nest Hub (2nd gen), Nest Wifi
  • Amazon Eero routers (Border Router)
  • Nanoleaf, Eve, Wemo Thread devices
  • Matter-over-Thread bulbs, plugs, sensors
  • Nordic / Silicon Labs / TI SoCs inside
Silicon reality: many modern SoCs are multiprotocol — the SAME chip can run Zigbee, Thread and BLE, chosen in firmware.

## Slide 28
Where This Is Heading (Future)
What to expect over the next few years
802.15.4 · Zigbee · Thread — Technical Masterclass
28
▸ Thread + Matter become the default for new smart-home products
  • IP-native, multi-admin (one device, many ecosystems), no proprietary hub lock-in
▸ Zigbee keeps a massive installed base and low-cost advantage
  • Continues in lighting, retail, industrial; bridges expose Zigbee devices into Matter
▸ Convergence via multiprotocol silicon
  • One SoC runs Thread + Zigbee + BLE; OTA can even switch protocols in the field
▸ Thread 1.3+ and beyond
  • Native Matter support, better Border Router roaming, larger/credentialed networks, improved reliability
▸ Bluetooth stays complementary
  • BLE for commissioning + phone proximity; Thread/Zigbee for the always-on mesh backbone
▸ Product strategy takeaway: build on multiprotocol SoCs, ship Matter-over-Thread, keep a Zigbee bridge path for legacy.

## Slide 29
One-Page Cheat Sheet
Fast recall for technical discussions
802.15.4 · Zigbee · Thread — Technical Masterclass
29
▸ 802.15.4
  • PHY+MAC, 2.4 GHz, 250 kbps, 127-byte frames, mesh-capable
▸ FFD / RFD
  • Full-function (can route) vs reduced-function (leaf/sleepy)
▸ PAN ID
  • 16-bit network identifier
▸ Zigbee roles
  • Coordinator / Router / End Device
▸ Cluster
  • Feature module: attributes (state) + commands (actions)
▸ Binding
  • Direct client→server link (switch→bulb)
▸ Thread roles
  • Leader / Router / REED / End Device / Border Router
▸ Border Router
  • Bridges Thread ↔ Wi-Fi/Ethernet at IP level
▸ 6LoWPAN
  • Compresses IPv6 into 802.15.4 frames
▸ MLE
  • Mesh Link Establishment — maintains Thread routes
▸ Matter
  • App layer over Thread/Wi-Fi; clusters like Zigbee
▸ Security
  • AES-128-CCM* everywhere; DTLS/J-PAKE onboarding

## Slide 30
References & Further Reading
Sources consulted to build this deck
802.15.4 · Zigbee · Thread — Technical Masterclass
30
IEEE 802.15.4-2020 standard
https://standards.ieee.org/ieee/802.15.4/7029/
Connectivity Standards Alliance (Zigbee)
https://csa-iot.org/all-solutions/zigbee/
Zigbee Specification / Zigbee 3.0
https://csa-iot.org/developer-resource/specifications-download-request/
Thread Group — Thread technology
https://www.threadgroup.org/What-is-Thread/Overview
Thread Specification & Fundamentals
https://www.threadgroup.org/support#specifications
Matter (CSA) overview
https://csa-iot.org/all-solutions/matter/
OpenThread (Google) documentation
https://openthread.io/guides/thread-primer
RFC 4944 — IPv6 over 802.15.4 (6LoWPAN)
https://www.rfc-editor.org/rfc/rfc4944
RFC 6282 — 6LoWPAN header compression
https://www.rfc-editor.org/rfc/rfc6282
RFC 6550 — RPL routing (context)
https://www.rfc-editor.org/rfc/rfc6550
Silicon Labs — Zigbee & Thread fundamentals
https://www.silabs.com/wireless/zigbee
Nordic Semiconductor — Thread & Matter docs
https://developer.nordicsemi.com/
Texas Instruments — 802.15.4 SimpleLink
https://www.ti.com/wireless-connectivity/thread/overview.html
Espressif — Thread/Zigbee/Matter guides
https://docs.espressif.com/
Zigbee Cluster Library (ZCL) spec
https://csa-iot.org/developer-resource/specifications-download-request/
Wikipedia — Zigbee / Thread / 802.15.4
https://en.wikipedia.org/wiki/Zigbee

## Slide 31
You're ready.
802.15.4 gives the radio & link · Zigbee adds mesh + a rich device language · Thread adds IPv6 · Matter unifies the app layer. You can now follow the discussion, define products, and read the market.
Next step: skim the References slide, then pick one SoC vendor SDK and build a hello-world node.